## Slide 1: LhARA FFA magnet design
Ta-Jen Kuo
Supervisor: Jaroslaw Pasternak, Jean-Baptiste Lagrange
Imperial College London, STFC
02/09/24

## Slide 2
LhARA FFA
Variable input energy by changing value of magnetic field
(multiple ions are possible)
Variable extraction energy at fixed geometry
Number of Cells | 10
K index | 5.23
Spiral angle (degrees) | 53.9
R0 (m) | 3.477
B0 (T) | 1.405
Packing factor | 0.34
Parameters at highest energy (15-127MeV)

## Slide 3
Magnetic field required
The goal is to have constant tune during acceleration
Arrange the integrated field with the ’Scaling Law’:
where is the integrated field at the reference radius 𝑟0, 𝑘 the integrated field index defined as:

## Slide 4
How is the scaling law achieved
A main coil provides the dipole field
Trim coils cross the pole face at constant radii and return around the side of the pole.
Gradient of the magnetic field achieved by adjusting the set of currents through the coils
Trim coils
Main coil
(Shown without the clamps and yoke in this image)

## Slide 5
Modelling in OPERA-3D
H type magnet with inner and outer return yokes
Field clamps, connected to the pole, following the spiral equation to control the fringe field
Coils in red wrapped around the pole
Inner return yoke
Outer return yoke
Field clamp
Field clamp

## Slide 6
Bz on the midplane with constant radius varying theta
In the 3D Opera model, sweeping through theta obtain Bz on midplane at a particular radius
Repeat of different radius to obtain integrated B field at different radii

## Slide 7
Field error from optimizing integrated B field
Central scenario: BL0 : 1.44 Tm , r0 :3.477m, k : 5.23 (15 – 127 MeV)
Oscillation in residuals due to
The discretization of trim coils

## Slide 8
Integrated k index after optimisation

## Slide 9
Bz on the midplane with constant radius varying theta
Part of the pole reaching 2.66T
Flat top of field distorted at higher radii due to
Saturation and will have an impact to the tune

## Slide 10
The vertical tune can be further controlled by adjusting the
Vertical aperture of the clamps
Aperture of clamp increases at larger radii

## Slide 11
Tune from optimizing integrated B field

## Slide 12
Power Consumption for magnet
Total power for one magnet: 43.2 kw, 10 magnets in a ring: 432 kw
Trim |  |  |  | Main |  |  | 
Coil width | 0.01 | m |  | Coil width | 0.075 | m | 
Coil height | 0.0925 | m |  | Coil height | 0.117 | m | 
Coil area | 0.000648 | m^2 |  | Coil area | 0.006143 | m^2 | 
Cu Resistivity | 1.68E-08 | Ohm.m |  | Cu Resistivity | 1.68E-08 | Ohm.m | 
Trimcoil | Length (m) | Current (AT) |  | Resistance (Ohm) |  | Power (W) | 
0 | 4.812 | 16545.03586 |  | 1.32E-05 |  | 3.60E+03 | 
1 | 2.37 | 6908.102679 |  | 6.14E-05 |  | 2.93E+03 | 
2 | 2.61 | 4795.473091 |  | 6.77E-05 |  | 1.56E+03 | 
3 | 2.85 | 3883.575168 |  | 7.39E-05 |  | 1.12E+03 | 
4 | 3.09 | 3184.744926 |  | 8.02E-05 |  | 8.14E+02 | 
5 | 3.33 | 2674.097645 |  | 8.65E-05 |  | 6.18E+02 | 
6 | 3.58 | 2250.996819 |  | 9.28E-05 |  | 4.70E+02 | 
7 | 3.82 | 1921.652039 |  | 9.90E-05 |  | 3.66E+02 | 
8 | 4.06 | 1653.689303 |  | 1.05E-04 |  | 2.88E+02 | 
9 | 4.30 | 1449.587291 |  | 1.12E-04 |  | 2.34E+02 | 
10 | 2.77 | 6908.102679 |  | 7.20E-05 |  | 3.43E+03 | 
11 | 3.02 | 4795.473091 |  | 7.82E-05 |  | 1.80E+03 | 
12 | 3.26 | 3883.575168 |  | 8.45E-05 |  | 1.27E+03 | 
13 | 3.50 | 3184.744926 |  | 9.08E-05 |  | 9.21E+02 | 
14 | 3.73 | 2674.097645 |  | 9.69E-05 |  | 6.93E+02 | 
15 | 3.98 | 2250.996819 |  | 1.03E-04 |  | 5.23E+02 | 
16 | 4.22 | 1921.652039 |  | 1.10E-04 |  | 4.05E+02 | 
17 | 4.46 | 1653.689303 |  | 1.16E-04 |  | 3.17E+02 | 
18 | 4.70 | 1449.587291 |  | 1.22E-04 |  | 2.56E+02 | 
 |  |  |  |  |  | Total Power (W) | 
 |  |  |  |  |  | 2.16E+04 | 

## Slide 13
Performance at different energy range
For the LhARA machine, we would like to accelerate beams at different energy while
being at the same tune point.
This can be done by scaling the BL0 value in the integrated field
Setting BL0 to of the original value, 6- 57 MeV energy range

## Slide 14
Tune from optimizing integrated B field

## Slide 15
Tune at different energy ranges

## Slide 16
Next Steps
Initial tune computed and looks promising
Need to check dynamic aperture
The real magnet might have larger errors in tune comparing to the simulation results
Investigate whether further tune spread reduction is required.
Vertical tune spread reduction: Further optimize aperture and position of clamps
Horizontal tune spread reduction: Increase number of power supplies to run different sets of current for the two layers of trim coils.