## Slide 1
LhARA Collaboration Meeting
WP6 - Design & Integration: Status
William Shields
(william.shields@rhul.ac.uk)
2nd September 2024

## Slide 2: Outline
Stage 1 update (me)
Stage 2 FFA design update (Ta-Jen)
Engineering & Integration (Clive)

## Slide 3
Overview: Layout
Locations and key dimensions defined :
  Gabor lens
  Arc magnets
  RF cavities
  Collimators
  Corrector magnets
  Vacuum valves
  Wall current monitors
Locations and key dimensions defined :
  Profile monitors
  Shielding walls
  Radiation shutters
  Octupole
  Beam dump
  Stage 2 switching magnet

## Slide 4
Overview: Key Parameters
Parameter | Value/Range | Unit
Laser Parameters Power Energy Pulse length Rep. rate Proton Energy Ion Energy | 100 2.5 25 10 15 3.77 | TW J fs Hz MeV MeV/u
Proton & Ion Capture Beam Divergence at design energy Gabor Lens effective length Gabor Lens physical length* Cathode Radius Maximum Voltage Number of Gabor Lenses* Alternative technology: solenoid length Alternative technology: solenoid max field | 11 0.857 1.157 0.0365 65 2 1.157 1.4 | degrees m m m kV m T
Stage 1 Beam Transport Number of Gabor lenses Number of re-bunching cavities Number of collimators Arc bending angle Number of bending magnets Maximum dipole field Number of quadrupoles Maximum quadrupole field Number of octupoles Beam pipe radius | 5 2 2 90 2 0.55 6 0.65 1 0.0365 | Degrees T T m

## Slide 5
Parameterised Source Distribution
LhARALinearOptics
  K. Long, M. Maxouti, N. Dover
  Code for modelling LhARA beam lines
  Optics, losses, particle source
Angular distribution generated as a cone centred on the normal to the foil surface.
  The opening angle of the cone taken from:
  Low KE angle taken to be 20°, linearly decreases such that angle at Emax is 5° (based on [1]).
  The distribution of the polar angle, θs, approximated as Gaussian
  11° at 15 MeV (25 MeV Emax)
[1] F. Nurnberg, M. Schollmeier, et al., Review of
Scientific Instruments 80 no. 3, (03, 2009) 033301

## Slide 6
Parameterised Source Distribution
KE spectrum from [2], unable to predict cut-off KE:
Model in [3] has cut off given by:
Probability of particle generated in E -> E+dE:
[2] J. Fuchs, P. Antici, et al.,” Nature Physics 2 (01, 2006)
[3] J. Schreiber, F. Bell, et al., Physical review letters 97 (08, 2006) 045005

## Slide 7
LhARA Linear Optics

## Slide 8
Beam Comparison To SCAPA Simulation

## Slide 9
Reduced Divergence Comparison
Test: theta distribution reduced by factor 4

## Slide 10
Stage 1 Nozzle
Methodology
  Generate beam (LLO)
  Track 5cm
  2mm radial filter
  Track 5cm with space charge
  2.87mm radial filter
Beam Property | OSIRIS SCAPA Simulation |  | Parameterised Beam, θs = 11° |  | Parameterised Beam, θs = 2.75° | 
 | Horizontal | Vertical | Horizontal | Vertical | Horizontal | Vertical
TWISS ⍺ | -199 | -209 | -355 | -357 | -341 | -342
TWISS β (m) | 19.65 | 20.60 | 35.35 | 35.51 | 33.89 | 33.93
Emittance (m rad) | 8.53e-08 | 8.11e-08 | 5.91e-8 | 5.87e-8 | 5.77e-8 | 5.75e-8
Beam Size (m) | 1.28e-03 | 1.28e-03 | 1.43e-3 | 1.43e-3 | 1.39e-3 | 1.40e-3
Transmission (%) | Nozzle Entrance | Nozzle Exit
OSIRIS SCAPA Simulation, | 88.7 | 68.0
Parameterised Beam, θs = 11° | 7.9 | 4.1
Parameterised Beam, θs = 2.75° | 87.5 | 55.9

## Slide 11
Stage 1 Beam at the Nozzle Exit
Final 15 MeV ± 2% beam for particle tracking simulations
Small differences in beam properties depending on particle count (% level)
  Good agreement at nozzle entrance – likely a space charge effect.

## Slide 12
Stage 1: Capture and Energy Selection
Solenoid (%) | SCAPA OSIRIS Simulation |  | Theta S = 11 |  | Theta S = 2.75 | 
 | KS (m-1) | B (T) | KS (m-1) | B (T) | KS (m-1) | B (T)
GL1 | 2.4917 | 1.4 | 2.4917 | 1.4 | 2.4917 | 1.4
GL2 | 1.0187 | 0.5724 | 1.0168 | 0.5713 | 1.0175 | 0.5717
GL3 | 1.4485 | 0.8138 | 1.4486 | 0.8139 | 1.4486 | 0.8139

## Slide 13
Stage 1 Optics Flexibility
Flexibility preserved for delivering 1-3 cm spot sizes.

## Slide 14
Gabor Lens Strengths
Beam Size , 2 σ diameter (cm) | Solenoid 4 B Field (T) | Solenoid 5 B Field (T) | Solenoid 6 B Field (T) | Solenoid 7 B Field (T)
1.0 | 0.7727 | 0.8222 | 4.466e-03 | 1.3746
1.5 | 1.0893 | 0.7576 | 1.1466 | 0.0382
2.0 | 1.1654 | 0.7032 | 0.9633 | 0.2220
2.5 | 1.1491 | 0.7637 | 0.8972 | 0.2634
3.0 | 1.2804 | 0.6017 | 0.7816 | 0.2048

## Slide 15
Stage 1 Optics for Stage 2 Operation
Challenges meeting baseline injection line beam parameters
  Emittance ~4.3e-6, beta of 50m = 1 sigma beam radius of 1.46 cm.
Solutions prioritising alpha = 0
Solution | Solenoid 4 B Field (T) | Solenoid 5 B Field (T) | Solenoid 6 B Field (T) | Solenoid 7 B Field (T)
1 | 1.0719 | 0.8482 | 0.7448 | 0.4998
2 | 1.0976 | 0 | 0 | 0.1176
Solution 1:
Alpha x: -0.09
Alpha y: -0.11
Beta x: 17.92
Beta y: 18.01
Emit x: 4.30e-06
Emit y: 4.29e-06
Solution 2:
Alpha x: -0.112
Alpha y: -0.169
Beta x: 17.49
Beta y: 17.37
Emit x: 3.22e-06
Emit y: 3.235e-06

## Slide 16
Beam at the Stage 1 End Station
Symmetric, circular, parallel beam.
  3.6cm spot size
Small growth in energy spread due to space charge
Uniform spectrum and temporal profile

## Slide 17
Summary
Standard parameterised source developed
Stage 1 performance unaffected
No other stage 1 changes
Ready for CDR write-up.

## Slide 18
Thank you
William Shields
william.shields@rhul.ac.uk