## Slide 1: LhARA the Laser-hybrid Accelerator for Radiobiological Applications

## Slide 2: The LhARA initiative
Vision:
Transform clinical practice of proton/ion-beam therapy by creating a fully automated, highly flexible system to harness the unique properties of laser-driven ion beams

## Slide 3: The case for fundamental radiobiology
Relative biological effectiveness:
  Known to depend on:
    Energy, ion species
    Dose, dose rate, spatial fractionation
    Tissue type
    Biological endpoint
Yet:
  p-treatment planning uses 1.1
  Effective values are used for C6+
Maximise the efficacy of PBT

## Slide 4: Radiobiology in new regimens
The ideally flexible beam facility can deliver it all!
 substantial opportunity for a step-change in understanding!
Time
domain
Space
domain
Energy
Ion
species
In combination and with chemo/immuno therapies
Multidisciplinary approach essential

## Slide 5: Laser-hybrid Accelerator for Radiobiological Applications
A novel, hybrid, approach:
Laser-driven, high-flux proton/ion source
  Overcome instantaneous dose-rate limitation
    Capture at >10 MeV
  Delivers protons or ions in very short pulses
    Bunches as short as 10—40 ns
  Triggerable; arbitrary pulse structure
Novel “electron-plasma-lens” capture & focusing
  Strong focusing (short focal length) without the use of high-field solenoid
Fast, flexible, fixed-field post acceleration
  Variable energy
    Protons: 15—127 MeV
    Ions: 5—34 MeV/u
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 6: LhARA to serve the Ion Therapy Research Facility
To serve ITRF: 2 + 3-year project in 6 work packages:
  Project Management
  Laser-driven proton and ion source
  Proton and ion capture
  Real-time dose-deposition profiling
  Novel, automated, end-station development
  Facility design and integration
2-year Preliminary Activity – Project start 01Oct22: CCAP-TN-10
2-year preliminary phase;
Flagged need for further 3-year preconstruction phase
First two years of “Full five-year proposal”
CCAP-TN-10

## Slide 7
 compact, uniquely flexible facility
N. Bliss (DL)
Draft
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738
N. Bliss et al

## Slide 8: Low-energy in-vitro end station
Maximum rep rate 10 Hz
  With current specification
Realisation of full scientific potential requires:
  Automation
  Novel instrumentation:
    High dose rate
    Spatial fractionation
    “Readout” in < 0.1s

## Slide 9: Conclusions
Laser-driven sources are disruptive technologies …
  With the potential to drive a step-change in clinical capability
Laser-hybrid approach has potential to:
  Overcome dose-rate limitations of present PBT sources
  Deliver uniquely flexible facility:
    Range of: ion species; energy; dose; dose-rate; time; and spatial distribution
  Be used in automated, triggerable system → reduce requirement for large gantry
    Disruptive/transformative approach to “distributed PBT for 2050”
Peer-group consultation critical:
  Maximise scientific potential through:
    Automation
    Novel techniques, instrumentation, operation, procedures …

## Slide 10: Beyond today
Peer-group essential preparation for bid for continuation:
  Start from and extend:
    Full five-year proposal
Target UKRI cross-council call to secure resource for multidisciplinary end-station development activity
Wave 4:
Call opens: 02Oct23
Decision. : 01Mar24
Funding : 01Oct24