## Slide 1
LhARA Collaboration Meeting #4
WP1.6: Design & Integration:
Stage 1 Design
William Shields
(william.shields@rhul.ac.uk)
20th September 2023

## Slide 2: Outline
Beam and baseline design performance review
7 Gabor lens configuration
Optimised optics & spot size flexibility
Beam uniformity
Dose delivery validation

## Slide 3
Re-simulated Beam Parameters
 | Pre-CDR Beam | Smilei Sampled Beam | SCAPA Beam (6 month report) | SCAPA Beam (updated)
Mean RMS emittance [m] | 3.26x10-7 | 1.43x10-8 | 7.98x10-8 | 8.25x10-8
Mean beta [m] | 4.89 | 141.34 | 21.62 | 20.24
Mean alpha | -50.22 | -1418.43 | -222.23 | -204.99
GPT simulation artefact discovered, artificial emittance growth
Target housing beam transport remodelled
Beam transport simulation drafted into technical note.

## Slide 4
SCAPA Beam: Full Spectrum
15 MeV ± 100 % beam
Excess at ~ 4 MeV
Constant bandwidth across transverse spatial distribution
  Suspected simulation artefact
Negligible impact on 15 MeV ± 2% region

## Slide 5
Co-propagating Beam Modelling
RF-Track: modelling composite beams with space charge forces
RF track example: 1000 protons & 1000 electrons (all macroparticles)
Aim: model LhARA proton & electron co-propagation in the target housing
Simulated electron data needed

## Slide 6
Baseline Design Performance
Optimised solutions for 3.6 cm and 3.2 cm beam. Smaller beams challenging.
No solutions for FFA injection line conditions.

## Slide 7
7 Gabor Lens Configuration
Investigation of 7 Gabor lens / solenoids configuration
Single energy collimator
Geometry modifications:
  Extra 0.2m between GL4 & GL5
  2.5m long drift after GL5
  GL6 & GL7 added in same configuration as GL4 & GL5
Matched solutions for 5 spot sizes (no space charge):
  3.0, 2.5, 2.0, 1.5, 1.0 cm (2 sigma diameter)
Baseline design update technical note drafted.

## Slide 8
Model Validation & Performance
Space charge impacting performance

## Slide 9
Capture Section Optimisation
Machine length flexibility between GL2 & GL3 achieved
  ~ 2.5 m
GL1
GL2
GL3
 | Original |  | Optimized | 
 | KS | B [T] | KS | B [T]
Gabor Lens 1 | 2.491764 | 1.4 | 2.491764 | 1.4
Gabor Lens 2 | 1.018776 | 0.572400 | 1.045545 | 0.587440
Gabor Lens 3 | 1.448605 | 0.813900 | 1.449852 | 0.814601

## Slide 10
Spot-size Optimisation
Optimised solutions found for 3.0, 2.5, and 2.0 cm spot sizes
Trending to divergent beam, focus after GL7.
Spot Size [cm] | Solenoid Equivalent Field [T] |  |  | 
 | Gabor Lens 4 | Gabor Lens 5 | Gabor Lens 6 | Gabor Lens 7
3.0 | 1.072940 | 0.807211 | 0.001191 | 0.787153
2.5 | 0.996313 | 0.832585 | 0.000871 | 0.858701
2.0 | 0.995976 | 0.823955 | 0.749300 | 0.836557

## Slide 11
Optimised Optics: Beam Profile
Similar end station profile and phase space to pre-CDR beam.

## Slide 12
2.0cm Spot Size: Arc Optimisation
Arc quadrupoles varied, improved solution for 2.0 cm spot size beam.
  Quad gradient constrained to ± 22.4 T/m (pole tip field = 0.82 T, 3.65cm radius)
Solutions for smaller spot sizes remains challenging.

## Slide 13
2.0cm Spot Size: Beam Profile
No major impact on end station beam profile.

## Slide 14
Matched Solution for FFA Injection Line
 | Optimized Solenoid Strength | 
 | KS | B [T]
Gabor Lens 4 | 1.82756 | 1.02682
Gabor Lens 7 | 0. 55688 | 0.31288
Beam Parameter | Value
Mean RMS Emittance [m rad] | 2.959 x 10-6
Mean Beta [m] | 49.92
Mean Alpha | 0. 075

## Slide 15
Preliminary Octupole Simulations
No octupole strength found producing sufficient uniformity over the spot size area.
Arbitrary K3 values shown.

## Slide 16
Repositioned Octupole: Arc End
Moving the octupole to the end of the vertical arc improves uniformity significantly.
Octupole strength to be optimised.

## Slide 17
Octupole Position Sensitivity
Artificial shift of mean vertical position entering the arc improved uniformity asymmetry.
Uniformity sensitive to beam position – correctors likely needed

## Slide 18
Dose Rate Check: End Station Model

## Slide 19
End Station Dose Rate

## Slide 20
Summary
Demonstrated flexibility of 7 Gabor lens configuration
Optimised solutions for spot sizes & FFA injection line
Re-established octupole feasibility
Validated end station dose calculations

## Slide 21
Thank you
William Shields
william.shields@rhul.ac.uk