## Slide 1: WP4: Ion-acoustic dose mapping
Maria Maxouti, Josie McGarrigle, Anthea MacIntosh-LaRocque, Vania Lay, Yu Hu, Ben Cox, Ben Smart, Colin Whyte, Kenneth Long, Emma Harris, Jeff Bamber

## Slide 2
2 Years
5 years
WP4: Ion-acoustic dose mapping
Validated models for the simulation of dose and ion-acoustic signals
Dose (J/kg)
Ioacoustic signal (Pa)
Scintillator signal (mV)
simulation
experiment
Experimental testing/evaluation of initial components for ion-acoustic and scintillation systems.
Biological sample holder designed for high throughput
Validated models for the simulation of dose and ion-acoustic signals for LhARA
Results from initial biology experiments
Ion-acoustic system for dose mapping on a pulse-by-pulse basis
Multi-element part spherical array
Dose map
Smart phantom system for cross-calibration of dose/range estimation
Lhara beams
Lhara beam
Angle from beam direction (deg)
Signal (Pa)

## Slide 3: 2-year Objectives,Tasks, Milestones
Objectives:
The development of a Geant4 MC simulation of the forward model
The development of a k-wave acoustic forward model
Tasks:
The detailed design of a proof of principle experiment to be executed during the Preconstruction Phase of the project, identifying potential suppliers for components.
Reports on progress towards above objectives.
Milestones:
18-month report: forward simulation of energy deposited in a water phantom (SmartPhantom) and deposited energy resolved in 4D.
24-month report: results of forward simulation and its use to optimise SmartPhantom performance to provide the power density spectrum as input to the acoustic model.

## Slide 4: Agenda
Jeff - Introduction, aims and objectives
Maria - Python BDSIM  Geant4 k-Wave simulation and plans for future validation experiment at LMU
Jeff - Photoacoustic simulation experiment (work of MRes student, Yu Hu)
Jeff – Summing up of status

## Slide 5: Preliminary photoacoustic “experimental simulation” – Yu Hu (MRes project)
Monte Carlo simulation
3-D dose distribution
Threshold and tessellate 3-D surface
3-D printer to produce mould
Optically absorbing gel phantom in the shape of the deposited dose distribution
Image using the photoacoustic system (part-spherical cup, and part-circular ring, arrays) at ICR
Evaluate received acoustic frequencies and reconstructed images in terms of analytical predictions and compare with k-Wave predictions

## Slide 6: Geant4 – 20000 protons, 40 ns, 70 MeV
z
x
y
water
protons
secondary particles
Kapton window
4 mm

## Slide 7: Further processing of deposited energy distribution
Radius (mm)
Threshold = 40% global peak
Threshold = 5% global peak
z (mm)
Relative z (mm)
Energy (MeV)
0 10 20 30 40
0 0.5 1.0 1.5 2.0 2.5 3.0
Radius (mm)
z (mm)
0 10 20 30 40 50
0 1 2 3 4
Radius (mm)

## Slide 8: Mould designs for beam insert and background impression, from surface of revolution from radius-depth plots
Two halves of beam insert
Mould to create a hollow impression in the background

## Slide 9: 3D printed mould examples (5%)
Two halves of beam insert
Half the beam hollow impression in half the cylindrical background

## Slide 10: Half phantom example (40%)
Background (TiO2 in gelatine)
Beam insert at 40% threshold (India ink pigmented)

## Slide 11: Photoacoustic imaging system
Acoustic sensor elements
1
256
128

## Slide 12: Example photoacoustic images (5%)

## Slide 13: Acoustic signals received at sensor element 128

## Slide 14: Acoustic signals received at sensor element 128

## Slide 15: Simulated acoustic signals received at sensor element 128

## Slide 16: Analytical (and experimentally confirmed) predictions of pressure-time waveforms
Energy delta function
Energy long Gaussian pulse
Parallel-sided slab
Cylinder
Sphere
c.f. experimental results
c.f. simulation radial profile
c.f. simulation results
Diebold et al, Phys Rev Let (1991)