## Slide 1
U. Schramm
Institute for Radiation Physics and Oncoray
Helmholtz-Zentrum Dresden-Rossendorf
Advancing Radiobiology Technology, IOP, London, 2023
Advancing laser accelerated proton beam performance
- for dose controlled irradiation studies
- and beyond the 100 MeV frontier

## Slide 2
Motivation
compact (cheap) accelerator to replace clinical proton therapy source
TNSA
exploit unique beam properties for high dose rate irradiation studies
(in the early times of laser plasma acceleration)

## Slide 3
Requirements (application ready laser ion accelerators)
application specific beam parameters
  energy to penetrate matter
  spectral yield (high dose rate)
beam transport (additional control) parameter monitoring
pulse repetition rate not target limited
reproducible conditions on demand
TNSA

## Slide 4
Requirements (application ready laser ion accelerators)
TNSA energy scaling
-> increase laser energy (power)
-> increase interaction efficiency

## Slide 5
Requirements (application ready laser ion accelerators)
TNSA energy scaling
-> short pulse lasers competitive
-> long pulse diode pumped …

## Slide 6
2020 Roadmap on plasma accelerators
New Journal of Physics 23, 031101 (2021)
Upscaling of laser accelerated proton beam energies …
from surface to efficient volumetric interaction
microscopic understanding (instabilities, …)
links between simulation and experiment, predictive capability, diagnostics
control (and knowledge) of laser parameters on target

## Slide 7
from surface to efficient volumetric interaction
microscopic understanding (instabilities, …)
links between simulation and experiment, predictive capability, diagnostics
control (and knowledge) of laser parameters on target,
pulse contrast (!)
Upscaling of laser accelerated proton beam energies …

## Slide 8: … through active dispersion (compression) management
(typically 15J (PM cleaned) on few 100nm plastic / formvar targets)
T. Ziegler, et al., Scientific Reports 11, 7338 (2021)
shift energy from pre- to
post-pulse side by TOD

## Slide 9: Stable laser proton accelerator operation over months @ >60 MeV
T. Ziegler, et al., Scientific Reports 11, 7338 (2021)
empirical GVD and TOD optimization improves and stabilizes TNSA performance
measured / cross-checked with RCF stacks,
TP spectromter, TOF
ready for applications

## Slide 10: Stable laser proton accelerator operation over months @ >60 MeV
T. Ziegler, et al., Scientific Reports 11, 7338 (2021)
empirical GVD and TOD optimization improves and stabilizes TNSA performance
measured / cross-checked with RCF stacks,
TP spectromter, TOF
ready for applications
irradiation of 5mm
deep volume

## Slide 11: Controlled dose delivery with pulsed solenoids
F. Brack, et al., Scientific Reports 10, 9118 (2020)
S. Busold, et al., (LIGHT), Sci. Rep. 5, 12459 (2015)
D. Haffa, et al., Sci. Rep. 9, 6714 (2019)
U. Masood, et al., Phys. Med. Biol. 62, 5531 (2017)
E. Beyreuther et al., PLOS ONE 12 (2017)
in vivo 3D irradiation (mouse ear tumor)
proof-of-concept study
criver.com
homogeneous dose
within 5×5×5 mm³
< 10% dose fluctuation
4 Gy in ~minute

## Slide 12
12,3 MeV
1 cm
18,6 MeV
2-solenoid Setup
vacuum
air
d [mm]
Dpulse [mGy]
RCF #
Single pulse depth dose control through polychromatic beams
F. Brack, et al., Scientific
Reports 10, 9118 (2020)

## Slide 13
2-solenoid Setup
vacuum
air
Single pulse depth dose control through on-shot metrology
M. Reimold, et al, Scientific Reports 12, 21488 (2022)

## Slide 14
2-solenoid Setup
vacuum
air
Single pulse depth dose control through on-shot metrology
    Enabling a full-scale pilot study in a small animal model with a laser proton beam
F. Kroll, et al., Nature Physics 18, 316 (2022)

## Slide 15
Accelerator readiness and stability benchmarked
F. Kroll, et al., Nature Physics 18, 316 (2022)
    Enabling a full-scale pilot study in a small animal model with a laser proton beam
Notes: Setup presented  now accelerator readiness/stability
Standard fig of merit in proton LPA and also precondition for exp.: cut-off/max. energy  stably > 60 MeV for many month  already unique performance in LPA
But to show readiness for radiobiological study: need to verify stability/readiness via model/application-specific parameters, here chosen e.g. pulse dose/homogeneity shown for days marked in green  grey areas mark targeted values  all within  first of its kind achievement
Next step: single shot resolution for one day (blue)  spectral stability from tof and depth dose homogeneity derived  all ok!!!
But: single shot dose fluctuates  inherent property of LPA source  mititigated via dose accumulation

## Slide 16
First in-vivo proton irradiation study with laser accelerated protons
F. Kroll, et al., Nature Physics 18, 316 (2022)
Monitor tumor growth control
(i.e. delayed tumor growth)
for different radiation sources
 | Draco PW | UPTD
mean dose | 3.9 | 3.9
single dose accuracy (2σ) | 8% | 14%
dose homogeneity lateral/depth (2σ) | 9%/< 9% | 9%/2%
mean dose rate | 1.2 – 2.2 Gy/min | 3.6 Gy/min
peak dose rate | 108 Gy/s | -

## Slide 17
First in-vivo proton irradiation study with laser accelerated protons
F. Kroll, et al., Nature Physics 18, 316 (2022)

## Slide 18
First in-vivo proton irradiation study with laser accelerated protons
    Full-scale pilot study in a small animal model with a laser proton beam
    Radiation induced (4 Gy) effect observed
    In total 47 mice at HZDR (Draco 4 Gy | Draco 0 Gy | X-ray 4 Gy | X-ray 0 Gy | Controll) + same number for reference at clinical beam
    Long-term survival unexpected, yet requiring higher statistics …
    Not a FLASH study
F. Kroll, et al., Nature Physics 18, 316 (2022)

## Slide 19
High dose rate effects (zebra-fish) ?
Controlled dose at highest precision
(mouse experiment, accumulated shots)
Maximum dose rate (up to 25 Gy/shot)
enabling FLASH irradiation studies
Draco laser system: single shot proton dose rate of 109 Gy/s
Reference study at UPTD using conventional proton dose rate

## Slide 20
Coming back to physics …
TNSA proton performance ready for demanding applications
But how to optimize volumetric interaction ?
How to tailor near-critical density targets ?
And serve repetition rate (self-replenishing target, without need for plasma mirrors)
-> Expanding foils and cryogenic hydrogen

## Slide 21
Coming back to physics …
Transparent target
pulse mostly transmitted
Dense, opaque target
mirror-like behaviour
pulse mostly reflected

## Slide 22
Coming back to physics …
Near critical density target
pulse mostly absorbed
over-critical
typ. > 1023 cm-3
typ. < 1020 cm-3
under-critical
1.7 x 1021 cm-3
ncritical[800nm]
near-critical
pre-expansion
foil
solid
hydrogen (jet)

## Slide 23
intrinsic target pre-expansion
enhanced proton energies at optimal thickness
onset of transparency at optimal thickness
comparison to other high-power laser systems
Pre-expanded thin foil studies at two laser systems w/o PM
N. Dover, T. Ziegler, et al.
Nature Light: Science and Appl. 12, 71 (2023)

## Slide 24
sorting by transmitted light
Proton emission characteristics
T. Ziegler, et al. unpublished

## Slide 25
Sample spectra (TPS and RCF data)
T. Ziegler, et al. unpublished

## Slide 26: Proton acceleration in near critical density targets
cryogenic hydrogen jet targets
with off-harmonic probing
S. Goede et al., PRL 118, 194801 (2017)
L. Obst et al., Sci. Rep. 7, 10248 (2017)
M. Gauthier, et al., APL 111, 114102 (2017)
L. Obst, et al., Nat. Comun. 9, 5292 (2018)
M. Loeser, et al, Optics Express 29, 9199 (2021)
T. Ziegler, et al., PPCF 60, 074003 (2018)
C. Bernert, et al., Sci. Rep. 12, 7287 (2022)
C. Bernert, et al., Phys. Rev. Appl. 19, 014070 (2023)

## Slide 27
enabling controlled plasma density tailoring and predictive simulation input
On-shot plasma characterization by bi-colour high resolution probing
M. Rehwald, C. Bernert, et al.,
Nat. Commun. 14, 4009 (2023)
20 ps
Pre-pulse
delay
30 ps
10µm
15µm

## Slide 28
- enabling quantitative simulation suggesting transition from TNSA via RTF-RPA to MVA
- supporting up to 80 MeV with debris-free and rep-rated target
On-shot hydrogen target density tailoring (with pre-pulse)
TNSA
MVA
RTF-RPA
M. Rehwald, C. Bernert, et al.,
Nat. Commun. 14, 4009 (2023)

## Slide 29
- enabling quantitative simulation suggesting transition from TNSA via RTF-RPA to MVA
- supporting up to 80 MeV with debris-free and rep-rated target
On-shot hydrogen target density tailoring
I. Goethel, et al., PPCF 64, 044010 (2022)
RTF-RPA = Relativistic Transparency
Front - RPA
synchronized acceleration of ions at the moving (intensity dependent) relativistic critical density front

## Slide 30
Repetition rate demonstration (at 1J / 5 Hz @ HIBEF)
Comprehensive set of diagnostics for target position (optical probing), laser-target overlap (p+ spectrometer, TOF, transmission screen), and laser pointing -> ready for machine learning applications
p-spectrometer (first 300 shots):
Relax beam
1J, 5Hz, 800nm
1.8 x 1020W/cm2
PS
optical probing
TS
H2 cryojet target
Proton cut-off distribution
(60% hits)
online target position monitor

## Slide 31
Proton acceleration take away message – pilot study demonstrates
system readiness – TNSA beaten with intrinsic laser setting – rep. rate
stability
cryogenic hydrogen
serving target rep rate
energy to penetrate volume
directed beam well exceeding 120 MeV
stability
long term and short term

## Slide 32
J. Pawelke, E. Beyreuther, K. Brüchner, E. Bodenstein, L. Karsch, E. Lessmann, M. Krause, E. Troost, N. Cordes, C. Richter, et al.
K. Zeil, J. Metzkes-Ng, F. Kroll, C. Bernert, E. Beyreuther, L. Gaus, S. Kraft, A. Nossula, M.E.P. Umlandt, M. Rehwald, M. Reimold,
H.-P. Schlenvoigt, M. Sobiella, T. Ziegler, S. Bock, R. Gebhardt, U. Helbig, T. Püschel, U. Schramm, T. Cowan, et al.
High-field laboratory Dresden (HLD) and HZDR workshop; R. Szabo, et al. (ELI-ALPS); J. Jansen, et al. (DKFZ)
Laser radiooncology
Laser particle acceleration
high power lasers Draco
and PENELOPE
laser-driven ion acceleration
computational radiation physics
biological models
reference beams
biological infrastructure
beam monitoring/ dosimetry
beam transport/ dose delivery

## Slide 33
K. Zeil, J. Metzkes-Ng, F. Kroll, S. Assenbaum, C. Bernert, F. Brack, M. Rehwald, M. Reimold, H.P. Schlenvoigt, T. Ziegler, et al.
A. Irman, J. Couperus, V. Chang, A. Ghaith, M. Laberge, et al.,
T. Kluge, A. Debus, M. Bussmann, R. Pausch, K. Steiniger, I. Göthel, M. Garten, et al.
J. Pawelke, E. Beyreuther, L. Karsch, M. Krause, et al.,
M. Siebold, D. Albach, S. Bock, R. Gebhardt, U. Helbig, M. Löser, T. Püschel, et al.
U. Schramm, T. Cowan, R. Sauerbrey
N. Dover, M. Nishiuchi, A. Kon, H. Kyriama et al. / M. Gauthier, F. Fiuza, S. Glenzer, et al. /
S. Goede, et al. / V. Malka, et al.

## Slide 35
Dresden (accelerator) platform (investigating FLASH requirements)
Reference
~ 4 min
0.13 Gy/s
~103 Gy/s
~109
Irradiation time
Mean dose rate
Pulse dose rate
Number of pulses
Maximum
Flash
~ 300 µs
105 Gy/s
~109 Gy/s
~4000
Isochronous cyclotron like Flash
~ 100 ms
320 Gy/s
~106 Gy/s
~106
Electron Linac/ Synchrocyclotron
like Flash
~ 164 ms
200 Gy/s
~109 Gy/s
5 x 800
Ref
UHDRsynclo
UHDRcyclo
UHDRMax
J. Pawelke, et al., Radiother. Oncol. 158, P7 (2021), L. Karsch et al. Radiother Oncol 173, 49 (2022)
100 ms
164 ms
Near arbitrary bunch sequence
at SRF accelerator ELBE (13 MHz bunch rate)
Total dose applied ~ 30 Gy
(laser accelerated protons reach 30 Gy / pulse)

## Slide 36
Dresden (accelerator) platform (investigating FLASH requirements)
same mean dose rate
different peak dose rate
Comparison of mean vs peak dose rate effects irradiating zebra-fish embryos at ELBE
J. Metzkes-Ng, E. Beyreuther, et al., The Dresden platform, in preparation